## Slide 1: Rethinking AIG Resynthesis in Parallel
DAC 2023
Presented by: 賈俊佑

## Slide 2: Outline
Introduction
Preliminaries
Method
  GPU-Parallel Refactoring
  GPU-Parallel Balancing
Experimental Results
Conclusion

## Slide 3: Introduction
AIG is widely used in logic optimization
AIG resynthesis combines multiple optimization algorithms in a sequence
- resyn2: b; rw; rf; b; rw; rwz; b; rfz; rwz; b
b = balancing
rw = rewriting
rf = refactoring
z = zero-gain
: reduce AIG level / delay
: replace small local subgraphs
: resynthesize larger logic cones
: allow non-worse replacement
resyn2 repeatedly applies balancing, rewriting, and refactoring

## Slide 4: Motivation
Large AIGs make resyn2 time-consuming
Previous work has accelerated rewriting on GPUs
  but resyn2 also includes refactoring and balancing
This paper parallelizes refactoring and balancing on GPUs
  enabling a full GPU-accelerated resyn2 flow

## Slide 5: Preliminaries - AIG and Cone
AIG
  internal nodes are 2-input AND gates
  edges may be complemented
Metrics
  area = number of AIG nodes
  delay = number of AIG levels
Cone
  local subgraph rooted at a node
  cut nodes are the inputs of the cone

## Slide 6: Background - AIG Refactoring
Refactoring optimizes larger local logic cones
Cone selection
  identify a local logic cone
Resynthesis
  rebuild an equivalent cone
Replacement
  replace the original cone if quality improves

## Slide 7: Fanout-Free Cone and MFFC
Fanout-Free Cone (FFC)
  internal nodes are not shared with outside logic
Maximum Fanout-Free Cone (MFFC)
  largest FFC of a root
Why FFC is useful
  replacing an FFC does not affect logic outside the cone
  disjoint FFCs can be processed independently

## Slide 8: GPU-Parallel Refactoring
Basic idea
- use disjoint FFCs as independent optimization units
Three-stage flow
  Identify and collapse disjoint FFCs
  Resynthesize collapsed FFCs in parallel
  Replace positive-gain cones in parallel

## Slide 9: Stage 1: Identify and Collapse Disjoint FFCs
Frontier = current roots to be processed
Start from primary outputs
For each node in the frontier:
  find its fanout-free cone
  collapse the cone into a local Boolean function
Cone inputs become the next frontier
Repeat from POs to PIs

## Slide 10: Stage 2: Parallel Resynthesis
Resynthesize collapsed FFCs in parallel
Compute gain after resynthesis
Keep positive-gain cones for replacement

## Slide 11: Stage 3: Parallel Replacement
Insert new nodes synchronously in parallel
  one thread per cone
  global synchronization between insertion steps
Replace old cone roots with new roots

## Slide 12: GPU-Parallel Hash-table
Structural hashing
  use fanins and inversion status as keys
  avoid duplicated nodes and enable logic sharing
Insertion issue
  the same key may be inserted more than once
GPU hash-table solution
  supporting batched node insertion and retrieval

## Slide 13: Background - AIG Balancing
Balancing reduces AIG level / delay
Collapse
  identify n-input AND-tree structures
  e.g., node 3 → AND(d,e,f,g)
Recursive balancing
  balance cut nodes and obtain their delays
Reconstruction
  rebuild the AND-tree in ascending delay order

## Slide 14: GPU-Parallel Balancing
Stage 1: Collapse
  identify n-input AND subtrees
  process level by level from POs to PIs
  store collapsed subtrees for reconstruction
Stage 2: Reconstruction
  rebuild collapsed AND subtrees
  process level by level from PIs to POs
  reconstruct same-level AND subtrees in parallel

## Slide 15: Experimental Setup
Baseline:
  original ABC sequential resyn2 flow
Benchmarks:
  enlarged EPFL combinational benchmark suite
  enlarged control circuits from the IWLS 2005 benchmark suite
Evaluation metrics:
  runtime speedup
  AIG area: number of nodes
  AIG delay: number of levels

## Slide 16: Experimental Results - Speedup and QoR

## Slide 17: Experimental Results - Scalability
Speedup increases as AIG size grows
GPU acceleration becomes effective for AIGs with more than 30K nodes

## Slide 18: Conclusion
Proposed GPU-parallel algorithms for AIG refactoring and balancing
Integrated with GPU rewriting to accelerate the full resyn2 flow
Full GPU resyn2 achieves:
  45.9× speedup over ABC resyn2
  comparable QoR